## Slide 1: VIC CALIBRATION FOR HYDROLOGICAL EXTREME MONITORING
Kel Markert
NASA-SERVIR Mekong Regional Associate
University of Alabama in Huntsville | Earth System Science Center
8 March 2017

## Slide 2: OUTLINE
  VIC Variables to calibrate
  Calibration methods
    Land surface model calibration
  Calibration best practices
  Nyando basin model calibration
  Calibration discussions

## Slide 3: VARIABLES TO CALIBRATE
Five typical variables to calibrate for VIC
Other variables can be calibrated
  Snow partitioning, Energy balance terms, Land surface parameterization
Typical calibration is mostly focused on soil variables (movement of water through soils)
Variable | units | Description | Typical Range
Ds | % | Fraction of Dsmax where non-linear baseflow occurs | >0 -1
Dsmax | mm・day-1 | Maximum baseflow that can occur from the lowest soil layer | >0 - ~30
Ws | % | Fraction of maximum soil moisture where non-linear baseflow occurs | >0 - 1
binf | n/a | Shape parameter of the VIC curve | >0 – 0.4
Soil depths (for each layer) | m | Soil depth in meters for each soil layer | 0.1 – 1.5

## Slide 4: VARIBLE CALIBRATION EFFECTS
With a higher value of Ds, the baseflow will be higher at lower water content in lowest soil layer
A higher value of Ws will raise the water content required for rapidly increasing, non-linear baseflow, which will tend to delay runoff peaks
A higher value of binf gives lower infiltration and yields higher surface runoff
Soil depth effects many model variables
  For runoff considerations, thicker soil depths slow down (baseflow dominated) seasonal peak flows and increase the loss due to evapotranspiration

## Slide 5: CALIBRATION METHODS
Manual calibrations
  Very time consuming
  May not provide the best parameters
  Based on regional knowledge
Computer calibrations
  Computationally intensive
  Time consuming (no user involvement)
  Very complex
  Provides well calibrated parameters (depending on algorithm used)
A focus of research is on more effective parameterization and calibration methods for hydrologic models

## Slide 6: CALIBRATION METHODS
Brute force calibrations
Random autostart complex
  Initialization based on random combination of parameters
  Uses best combination of parameters to start the simplex minimization algorithm to optimize
Genetic optimization
  Based on the laws of natural selections
  Initializes with random set of parameters and randomly chooses “parent” sets based on performance
  Combines “parent” parameters to create “children”
  Iterates for n number of generations

## Slide 7: CALIBRATION METHODS
Multi-Objective Complex Evolution (MOCOM-UA)
  Developed to calibrate models efficiently on multiple evaluation functions
  Larger optimization populations produce a more complete picture of the Pareto set but also increase the number of simulations
Shuffled Complex Evolution (SCE-UA)
  Most commonly used calibration algorithm for hydrologic applications
  Designed to find the global optima
  Starts several chains/complexes that evolve individually then shuffles parameters to make new complexes

## Slide 8: CALIBRATING NYANDO BASIN
We are going to perform a calibration on the Nyando basin model
Update the global parameter simulation time for 2005-2009
Navigate to the scripts folder in terminal
Run the command: $ python calibrate_vic.py 15
  This executes a random parameter set estimation calibration for 15 iterations
A more robust calibration script is provided (calibrate_vic_sceua.py)
  Requires more complex set-up and interpretation of results

## Slide 9: CALIBRATION BEST PRACTICES
Necessary to have an independent record for calibration and validation (or evaluation) of the hydrologic simulation
  Typically save approximately half of observed time series for validation
Calibrate by sub-basin and combine for entire region
Common observation to use for calibration is streamflow
  Can calibrate model using other observed parameters (soil moisture, ET, snow depth)
  In situ measurements vs satellite observations

## Slide 10: CALIBRATION FOR NYANDO BASIN
Used the SCE-UA algorithm
  Parameter populations of 500 each running 55 simulations with one chain (12 hour runtime)
Uncalibrated NSE: 0.42
Calibrated NSE: 0.72
  Bias: -1.11 m3·s-1
  RMSE: 6.80 m3·s-1

## Slide 11: NYANDO BASIN MODEL VALIDATION
Model over/under estimates peak flow
  Possible errors with input precipitation dataset fjkal
Uncalibrated NSE: 0.48
Calibrated NSE: 0.55
  Bias: -6.07 m3·s-1
  RMSE: 10.89 m3·s-1

## Slide 12: EFFICIENT CALIBRATION TIPS
Grid cells with vegetation classes that cover less than 1-2 % of the grid cell can be removed
  Should not be done when evaluating changes in streamflow as a function of change in vegetation
Only calibrate on wet pixels (grid cells that receive high precipitation and significantly contribute to streamflow)
Calibrate model using a large grid cell (~1°) and extract parameters to smaller grid for simulations
  Significantly decreases calibration time
Calibrate using water balance mode

## Slide 13: ADVANCED CALIBRATION METHODS
Spare grid calibration
  Randomly selected calibration grid cells
  Spatially interpolate calibrated factors
  Based on monthly spatially homogeneous values (runoff ratio) at the pixel level
    No need for long-term streamflow or routing model
  Used to calibrate the NLDAS model
(Troy 2008, Open access article in Water Resources Research) Volume 44, Issue 9, W09411, 6 SEP 2008 DOI: 10.1029/2007WR006513 http://onlinelibrary.wiley.com/doi/10.1029/2007WR006513/full#wrcr11550-fig-0001

## Slide 14: CALIBRATION CONSIDERATIONS
Calibration methods depends on the application of the model
  Includes data used calibrated against (e.g. streamflow forecasting model should be calibrated against observed streamflow)
  Calibrating against observed streamflow does not necessarily mean ET or snow depth may be calibrated
Calibration results and can be limited by input data quality
  Calibration can only go as far as the model and data allows
Operational models should be calibrated regularly
Daily streamflow requires further calibration of the routing model parameters

## Slide 15: THANK YOU
Kel Markert
kel.markert@nasa.gov